## Slide 1
Quality Control in Manufacturing: Defect Inspection System
Image Processing & Computer Vision (IPCV) • Classical Vision Pipeline on MVTec AD Bottle Dataset
MOTILAL NEHRU NATIONAL INSTITUTE OF TECHNOLOGY ALLAHABAD
Department of Computer Science & Engineering
UNDER THE GUIDANCE OF
Prof. Abhimanyu Sahu
PROJECT TEAM
Manjeet Kumar (20233179)
Md Abdul Kalam (20233183)
Lokesh Kumar Kankarwal (20233175)
Sanginesh Singh (20233251)

## Slide 2
Why Classical Computer Vision?
CORE OBJECTIVES
Robust Alignment • Multi-Channel Extraction • 3-Tier Risk Engine • Streamlit Dashboard
Defect Imbalance
Real plants rarely see fractures.
Trained strictly on 209 normal bottles.
Zero GPU Footprint
Runs entirely on standard laptop CPU.
Sub-30 ms latency per frame.
Full Interpretability
No unexplainable neural black box.
Explicit pixel and edge anomalies.
This project builds a highly accurate, CPU-friendly visual inspection system using classical CV algorithms that learns to detect cracks and dirt by studying only 209 normal, defect-free bottles from mvtec-ad dataset.
THE PROBLEM & OUR SOLUTION
Manual bottle inspection is slow, costly, and unreliable. While deep learning is a popular alternative, it requires thousands of rare defect samples and expensive GPUs.

## Slide 3
SYSTEM ARCHITECTURE
End-to-End Pipeline Workflow
OFFLINE TRAINING FLOW
209 Normal Bottles • Rapid CPU Moment Estimation (~3.5s)
ONLINE INSPECTION FLOW
Real-Time Factory Edge Inference (~28 ms / frame)
Affine Drift Correction
Cancels conveyor belt displacement to sub-pixel coordinates across both training and inference.
One-Class Statistical Distribution
Fits spatial mean and variance solely on 209 defect-free samples, eliminating the need for defective training data.
STEP T1
Normal Image Ingestion
209 defect-free 900x900 bottles downsampled to 300x300.
STEP T2
Canonical Alignment
Centroid localization and affine warp translation to (150, 150).
STEP T3
9-Ch Feature Tensor
Color (LAB, HSV), edges (Sobel, Laplacian), texture & morphology.
STEP T4
Statistical Modeling
Pixel-wise mean (μ) and regularized standard deviation (σ + ε).
STEP T5
Model Serialization
Export 3.8 MB compressed baseline archive (.npz artifact).
STEP I1
Input & Resizing
Conveyor frame resize to 300x300 area interpolation.
STEP I2
Circle Alignment
Enclosing circle center translation to coordinate (150, 150).
STEP I3
9-Ch Extraction
Matching 9-channel descriptor computation for test frame.
STEP I4
Mahalanobis Engine
Weighted Z-score residual map and 99.8th percentile scoring.
STEP I5
3-Tier Decision
Pass, Suspicious Review, or Reject with localized bbox.

## Slide 4
Channel | Feature Name | CV Operation | Target Defect | Sensitivity
0 | CIE-L* Lightness | Luminance / 255.0 | Opaque dirt and dark spots | Normal (1.0x)
1 - 2 | CIE-a* / CIE-b* | Green-Red & Blue-Yellow | Chemical stains & oil residue | High (1.2x)
3 - 4 | HSV Saturation / Value | Purity & Brightness | Liquid coatings & shadows | Very High (1.5x)
5 | Sobel Gradients (X, Y) | First-order gradient magnitude | Structural cracks & broken glass | Normal (1.0x)
6 | Laplacian Sharpness | Second-order derivative filter | Fine hairline cracks & rim chips | Normal (1.0x)
7 | Local Std Dev Texture | 7x7 local patch variance | Surface abrasions & roughness | Normal (1.0x)
8 | Top-Hat / Black-Hat | 9x9 morphological kernel | Glass flakes & dark dust specks | High (1.2x)
FEATURE ENGINEERING
9-Channel Feature Extraction

## Slide 5
QUALITY DECISION ARCHITECTURE
3-Tier Risk Decision Engine
TIER 1: PASS
Score < 16.0
Normal bottle, passes immediately.
TIER 2: REVIEW
16.0 ≤ Score < 18.5
Borderline cases routed to inspection.
TIER 3: FAIL
Score ≥ 18.5
Confirmed cracks, chips, or dirt.

## Slide 6
Defect Category | Test Samples | Pass (Good) | Review (Close Call) | Fail (Defective) | Performance Metric
Normal / Defect-free | 20 | 15 | 5 | 0 | 0.0% False Rejection
Broken Large (Fractures) | 20 | 0 | 0 | 20 | 100.0% Detection
Broken Small (Hairline) | 22 | 0 | 1 | 21 | 95.5% Defect + 4.5% Review
Contamination (Foreign) | 21 | 2 | 0 | 19 | 90.5% Detection
Overall Total | 83 | 17 | 6 | 60 | 98.69% ROC-AUC
QUANTITATIVE VALIDATION
MVTec AD Benchmark Results
Zero Scrap Waste
Zero normal bottles incorrectly thrown away.
Zero Escapes
100% of broken bottles caught by Fail or Review.

## Slide 7
System Metric | Our Classical IPCV Approach | Deep Learning (CNN / PatchCore)
Compute Hardware | Standard Laptop CPU (No GPU) | Dedicated NVIDIA GPU Required
Inference Latency | ~28 ms / image (35 FPS) | 60 – 200 ms / image
Model File Footprint | 3.8 MB (NumPy Array File) | 150 MB – 1.2 GB Weights
Training Duration | ~3.5 seconds on CPU | 15 – 45 minutes on GPU
Decision Explainability | 100% Transparent (Filters & Edges) | Black Box Latent Space
TECHNICAL COMPARISON
Classical IPCV vs. Deep Learning
Delivers industrial line throughput (35 FPS) without specialized edge hardware or complex training setups.

## Slide 8
PROJECT WRAP-UP
Conclusion & Future Scope
Motilal Nehru National Institute of Technology • Computer Science & Engineering
Thank You • Questions & Discussion
Key Project Outcomes
Future Directions
98.7% ROC-AUC: High detection accuracy.
Zero Scrap: 0% false rejection of good bottles.
Real-Time CPU: 35 FPS processing speed.
C++ Port: Target 100+ FPS line speed.
Multi-Angle Vision: Inspect bottom and neck simultaneously.
Edge Integration: Embed on conveyor PLC controllers.